## Slide 1: Object Distance Estimation Using Kinect Sensor
Andrea Bersellini

## Slide 2: Proof Of Concept

## Slide 3: Intrinsic Calibration
0
255
RGB VALUES
DISTANCES
0.5
4.5
90cm
120cm
m = (value1 - value0) / (calib_distance_1 - calib_distance_0)
dist0 = (0 - (value1 - m * calib_distance_1)) / m
dist255 = (255 - (value1 - m * calib_distance_1)) / m

## Slide 4: Extrinsic Calibration
RADIUS = 20
RADIUS = 25
scale_factor = depth_radius / color_radius

## Slide 5: Processing Pipeline
Calibration of the images
Coordinate point of the object
Depth information of the point
Distance of the object

## Slide 6: Final Results
LABLE | MEASURED | PREDICTED
Image 1 | 120 | 116
Image 2 | 152 | 151
Image 3 | 134 | 136
Image 4 | 71 | 71
Image 5 | 104 | 105

## Slide 7: Causes Of Error
Calibration Measurement Approximation
Non-linearity in Grayscale Value Mapping
Inconsistency of Kinect Image Acquisition

## Slide 8: Applications
Robotics Perception
Robotics Localization
Building
Design

## Slide 9: Thanks for the attention!